## Slide 1: Data Processing TMS Study
Joe Shaffer
December 2020

## Slide 2: Notes
These scripts are largely intended to run on Argon (hpc.iowa.edu) and are built to optimize using parallel resources to run. Some of the others are intended to run locally either within Matlab or through a linux/mac terminal.
This pipeline will require the installation of AFNI, Freesurfer, and Anaconda (with a Python 2 environment) to your Argon account.
Regression analysis and visualization also rely on Nifti Tools (https://www.mathworks.com/matlabcentral/fileexchange/8797-tools-for-nifti-and-analyze-image) and BrainNet viewer (https://www.nitrc.org/projects/bnv/) within Matlab
Copies of many of these scripts can also be found in my Github account: https://github.com/jjshaffer

## Slide 3
Download DICOMs from Xnat & convert to NIFTI in BIDS filestructure
(Project_name_data)
Compile Imaging and Demographic Data
Put Regression Results back together
Run Regression in Parallel
(by “slice”)
FDR Correction, thresholding
Make NIFTI images
Create “Bucket” for AFNI visualization
runPostProcessing.m
toBucket.sh
Xanalysis.m, batchXAnalysis.m
Data.mat
Demographics.txt
BrainMask.mat
CombineSubjectData directory
RegressionAnalysis directory
read_all_X.m
XPipeline directory
Run Preprocessing in parallel
(by subject)
xnat_downloader directory
readBIDS_forX.sh
runIterative_XDownloader.sh
Cluster submission scripts are all named iterativeClusterSubmit.sh and exist within relevant directories
Note: This step is the easiest target for future automation. It is currently labor intensive and fiddly

## Slide 4: Data Download
Find xnat in /mrrcdata/SCZ_TMS_TIMING/scripts/xnat_downloader or /mrrcdata/BD_TMS_TIMING/scripts/xnat_downloader
Edit the SUBJECTS array in runIterative_SCZ_TMSDownloader.sh or runIterative_BD_TMSDownloader.sh to include subject IDs of new participants (check xnat if you need IDs)
Activate a python 2 environment using anaconda i.e. conda activate mypython2 – if you don’t do this, xnat_downloader will fail. It cannot use python 3, so if you have loaded python 3 modules, this can also fail
Run the runIterative script you edited earlier for each subject while passing the index for the new subjects in the SUBJECTS array. This will require you to login to xnat in the terminal. You can create a config file containing your username and password, but I do not recommend storing that file on the data share.
If the scan names change (which happens sometimes with scanner updates), you can update your definitions in the .json configuration files; TMS_CRBL_12-31-2019.json (for BD) or TMS_SCZ_12-31-2019.json
This should download the data and convert it from DICOMs to .nii.gz images and place them in the BIDS format in the /mrrcdata/SCZ_TMS_TIMING/SCZ_TMS_data or /mrrcdata/BD_TMS_TIMING/BD_TMS_data directories. Within these folders, DICOMS are stored in /sourcedata while each participant will have a folder with subdirectories for each session, data type according to the BIDS format. You will want to double check that all of your data was downloaded correctly.

## Slide 5: Data Preprocessing
Note 1: Running many of these scripts on the cluster vs. locally may require editing one of the scripts to set the DATA_DIR variable. This is usually in the readBIDS… script, but also in the getSubjectIndex.sh script
$PROJECT_DIR is either /mrrcdata/BD_TMS_DATA or /mrrcdata/SCZ_TMS_DATA as appropriate. The datastructures are strongly parallel, with healthy control data stored in the SCZ project.
You will need to have AFNI and Freesurfer installed to your cluster account/environment to run these.

## Slide 6: Freesurfer/Rest
Scripts located in /mrrcdata/SCZ_TMS_TIMING/scripts/RestPipeline or /mrrcdata/BD_TMS_TIMING/scripts/RestPipeline
Edit the iterative submission line in iterativeClusterSubmit.sh to include the index # of the new subjects’ files in the data directory. These numbers shift as you download more data. You can use the getSubjectIndex.sh script to get a ballpark number, but this sometimes is off by 1 depending on when the “sourcedata” folder gets counted.
iterativeClusterSubmit.sh calls readBIDS_forRestingState2.sh which in turn calls run_FreeSurfer.sh, run_FreeSurfer_singleSession.sh, and/or run_afni_proc_rest
If you need to run less than the full analysis, editing readBIDS_forRestingState2.sh is probably your best bet

## Slide 7: Freesurfer/Rest
The readBIDS_forRestingState2.sh script essentially creates an array of filenames in the data directory and then runs analysis for the ith filename (subject ID) in that list. You can call this script directly by passing an integer to tell it which filename to run on in the command line.
For the appropriate subject, the script finds the appropriate anatomical and resting-state images, runs freesurfer, and then runs the resting-state analysis.
Note that for the TMS study, a T1 image is collected in the first session and a T2 in the second. run_FreeSurfer.sh accounts for this by aligning the T2 image to the T1 image and calling freesurfer with both. For subjects that drop out or where a T2 isn’t available, run_FreeSurfer_singleSession.sh is called instead, which only uses the T1.

## Slide 8: Freesurfer/Rest
The results of these will go into the $PROJECT_DIR/derivatives/FreeSurfer and $PROJECT_DIR/AFNI_Rest directories. You should check that all of the data is present. There should be a “SUMA” folder within FreeSurfer that has files within it and there should be a stats.errts… file within the AFNI_Rest directory for each subject/session.
Note: If processing fails for a given subject/session, you will need to delete the output directory for that subject/session and the generated script in the AFNI_Rest folder or else subsequent attempts will refuse to overwrite these outputs.

## Slide 9: T1rho Analysis
Scripts are located in $PROJECT_DIR/scripts/T1rhoPipeline
The format of this analysis parallels the Freesurfer/Rest analysis
Freesurfer MUST be performed first, or T1rho analysis will fail
iterativeClusterSubmit.sh runs the readBIDS_forT1rho.sh script which in turn calls processT1rho.sh
As before, you will need to edit iterativeClusterSubmit.sh to include the appropriate subject indices in the iterative submission line. These indices should be the same as in the RestPipeline
Output goes to $PROJECT_DIR/derivatives/T1rho

## Slide 10: Timing Task
The Behavioral data generated by ePrime is necessary for completing this step. There should be a file named TimingTaskRun#-SubjID-Session#.txt for each of the 4 runs, subject, and session (1 or 2)
  For example TimingTaskRun3-0671-1.txt is the file for the third run of the task for participant 0671 during their first imaging (pre TMS) session.
These files will need to be uploaded to the $PROJECT_DIR/BEHAV folder and sorted into folders for each subject and session (see the files already in this directory for an example)
The script moveBehavFiles.sh should be able to do this. You will need to pass the subject ID# (as written in the TimingTaskRun filenames). It uses the data directory to lookup the session numbers, so you will want to have downloaded the imaging data first. For controls – or for subjects from the Bipolar_R01, you will need to un-comment alternative definitions of the variable subjectID within the script to work correctly (i.e. set the CBM or CTL prefixes)

## Slide 11: Timing Task – Behavior Parsing
Once the data is sorted into these folders, scripts for parsing these behavioral files into the form that is needed for doing imaging analysis can be found in $PROJECT_DIR/scripts/FuncPipeline
Edit parseAllBehav.m in Matlab such that: Subject is an array of the full subject IDs (should match the data folder), Session is an array of the imaging session ID (should match the data folder), and SubjID matches the appropriate truncated Subject ID and session number that matches the ePrime file (letters aren’t allowed in ePrime subject IDs).
  For example, to parse TimingTaskRun3-0671-1.txt and TimingTaskRun3-0671-2.txt, we would set Subject = {‘CBM0671’, ‘CBM0671’}; Session = {‘20201112’, ‘20201120’}; SubjID = {‘0671-1’, ‘0671-2’};
parseAllBehav.m calls parseBehav.m which calls readTimingRun.m
Note: there are two “types” of conditions listed. The ones beginning with “o” are timed to match the onset of the stimulus, the ones beginning with “r” are timed to match the onset of the response. “f” = fixation, 0 = immediate response, 3 = 3second condition, 12 = 12 second condition

## Slide 12: Timing Task Image Preprocessing
Scripts are located in $PROJECT_DIR/scripts/FuncPipeline
Parallels the layout of the resting state analysis: iterativeClusterSubmit.sh is used to loop over the subject indices in readBIDS_forTimingTask.sh which calls run_afni_proc.sh
As before, you will need to update the iterative job loop in iterativeClusterSubmit.sh
Selecting Onset or Response requires commenting out/uncommenting the settings for the stimulus and output directories in run_afni_proc.sh
Outputs will be placed in $PROJECT_DIR/derivatives/TimingTask_Onset or $PROJECT_DIR/derivatives/TimingTask_Response

## Slide 13: Regression Analysis
Regression Analysis scripts are written in Matlab
Processing requires generating a .csv spreadsheet that lists the necessary demographic/clinical ratings for each participant and a matched .mat file that contains the appropriate imaging data. These files must match – i.e. the order of the subjects/sessions must match in order to ensure that the appropriate demographic information gets used with the correct imaging data
FMRI and T1rho analysis also requires a mask that indicates where brain voxels are located in the imaging data to avoid running regression models on non-brain voxels (which improves processing speed)

## Slide 14: Resting State
First compile pre-processed images into Matlab datafile – scripts are located within the CompilePreprocessedImagingData folder
  Edit read_all_netcc.m to include the scans you are interested in as an array for the variable SCANS. Generally there are two different lists, one for BD/SCZ(first session only) vs HC and one for the TMS effect with only BD/SCZ participants with a pre and post session. Uncomment the appropriate Outprefix value.
  For BD, you will also need to adjust the ctrl_index to match the first control participant’s index in the SCANS array because the control data is located within the SCZ project directories. NOTE: Controls must all appear at the end of the list for this index to work
  The outputs will be saved to the derivatives/AAL_RESULTS folder (if using another atlas, you may need to adjust the read_all_netcc file to change the matrix size variable).

## Slide 15: Resting State
Align any demographic data to the rows of the session list file generated by running read_all_netcc. Note that the column labels must be Subject, SessionID, Session, Group (1 for BD or SCZ, 0 for HC), Age, Sex (1 for male, 2 for female), and Treatment (0 = sham, 1 = TMS) in order to work correctly. Save a copy of this excel sheet as a tab-delimited .txt file.
Edit RestingStateAnalysis.m to appropriately reference the demographic.txt file and imaging data.m files and to perform the desired regression analysis. You will need to provide the null and experimental models using Matlab’s formatting. The scripts are currently set up to perform BD/SCZ vs HC with age, sex as covariates using 1st imaging scans and to perform TMS vs Sham as the interaction between Treatment and imaging session within the BD/SCZ group only for individuals who completed pre and post sessions. Additional comparisons may require more involved editing

## Slide 16: Resting State
To run the analysis, submit iterativeClusterSubmit.sh to the cluster or run locally (edit the DATA_DIR path as necessary and pass the desired row # to the function).
This will execute each row of the matrix in parallel. After this is completely you will need to put them back together using runPostProcessing.m, which will assemble the images, run FDR correction, and generate the needed files for visualizing with BrainNet

## Slide 17: Functions
combineConnectivityRows.m – puts all the slices from the regression analysis back together into a single matrix
makeAALMatrix.m – generates a figure showing the connectivity matrix for AAL atlas with summary labeling
runFDRCorrection.m – runs FDR correction on full AAL matrix
stripSelfCorr.m – can be used to reset the self-correlation line y = x
thresholdMaps.m – used to apply a threshold mask to the matrix
maskImage.m – used to apply a region mask to the matrix (e.g. AAL-cbmMask.mat, AAL-VermisMask.mat)
runMaskedFDRCorrection.m – runs FDR correction using a mask to exclude matrix entries that aren’t part of the mask from the calculation

## Slide 18: Timing Task – Compile Data
First compile pre-processed images into Matlab datafile – scripts are located within the CompilePreprocessedImagingData folder
  Edit copyAllFuncImages.sh to include required subjects and sessions and then run it. This script calls copyFuncImages.sh to convert the functional images from AFNI format to NIFTI and selects the relevant task comparisons from the functional data.
  Edit combine_Functional_Images.m to include the scans you are interested in as an array for the variable SCANS. You will want to choose the appropriate value for DATA_DIR as well. Run this by providing a contrast (‘L’, ‘I’, ‘F’, ‘S’, ‘L-I’, ‘L-F’, etc) and a prefix for the output file. This script relies on NIFTI Tools for Matlab and generates a data file, a csv that lists the subjects in order, and a consensus mask of brain areas included in those subjects (i.e. voxels included in >95% of participants). The files are generated within the derivatives/TimingTask_Onset (or Response) folder. For BD, you will need to provide an index for where in the list controls begin (and they must all be at the end of the list) because they are stored in the SCZ directory.

## Slide 19: Timing Task – Regression Analysis
Align any demographic data to the rows of the session list file generated by running read_all_netcc. Note that the column labels must be Subject, SessionID, Session, Group (1 for BD or SCZ, 0 for HC), Age, Sex (1 for male, 2 for female), and Treatment (0 = sham, 1 = TMS) in order to work correctly. Save a copy of this excel sheet as a tab-delimited .txt file
Edit TimingTaskAnalysis.m to appropriately reference the demographic.txt file and imaging data.m files and to perform the desired regression analysis. You will need to provide the null and experimental models using Matlab’s formatting. The scripts are currently set up to perform BD/SCZ vs HC with age, sex as covariates using 1st imaging scans and to perform TMS vs Sham as the interaction between Treatment and imaging session within the BD/SCZ group only for individuals who completed pre and post sessions. It is set up to do this in the Long – Immediate and Long – Fixation conditions. Additional comparisons may require more involved editing

## Slide 20: Timing Task – Regression Analysis
To run the analysis, submit iterativeClusterSubmit.sh to the cluster. This will run the analysis in parallel with 1 cluster job per “slice” by iterating on the x axis.
After analysis is complete, there will be 61 “slices” (each corresponding to an x index in the image. These slices can be put back together by using the combineSlices function. You will need to pass it the appropriate prefix (everything before “_slice …”) and the number of slices (61). This will generate a single 4d image matrix (x,y,z, statistical values).
Generating separate images for each statistical score can be done using makeImages.m. This will require that you provide a NIFTI image as a “template” because the NIFTI tools do not maintain appropriate header values. I generally use the timing task preprocessing “stats” file for one of the participants created by copyAllFuncImages.sh because it should be in the appropriate orientation and resolution as the template.

## Slide 21: Timing Task – Multiple Corrections
False Discovery rate correction can be performed using runFDRCorrection.m. This will require the image mask used to avoid correcting for non-brain voxels. Like makeImages.m, this will also require a NIFTI image as a template.
Several of these steps are combined in runPostProcessing.m. You will need to run toBucket.sh afterwards
Once this has been done, you can combine all of the different images that you are interested in using toBucket.sh. At a minimum you will want to include the t-statistic, 1-p value, and FDR-corrected 1-p value images for your variable of interest. You will need to edit the script to ensure the names are correct.
Once this has been done, you can use AFNI for visualization with the t-statistic as the “overlay” and the FDR corrected 1-p value image as the “threshold.”

## Slide 22: Alignment Issues
There are sometimes alignment issues between the functional image created by toBucket.sh and the desired anatomical image. If this occurs, you may need to use Afni’s 3dinfo to ensure that the orientations, template space, etc of these images match. These can be corrected with Afni’s 3drefit Remember that anatomical images are usually at 1mm3 voxel sizes while the functional images are in the 3-4mm3 range.

## Slide 23: T1rho
First compile the images – unlike the previous methods, the T1rho pipeline is able to read the Sessionlist files in order to generate the needed files. Copy the sessionlist .txt files you used for regression for resting state or the Timing Task to the scripts/T1rhoPipeline/CombineSubjectData directory and run createDataFile.m. Since these images are considerably larger, you can also use iterativeClusterSubmit.sh to do this on the cluster. For BD, you will need to also edit the Control Subject index where control subjects start in the spreadsheet (note, Controls need to be last in the list). However this approach does not yet create a mask file. You will need to make it with makeMask.m
You can also use read_all_T1rho.m just as previous scripts for compiling rest and TimingTask data. This will generate a mask.

## Slide 24: T1rho Regression Analysis
As before, T1rhoAnalysis.m needs to be edited to include the appropriate demographic .txt file, imaging data .mat file, and mask .mat file. Any changes to the regression model should be made here. If you add variables you will also need to edit batchT1rhoContrast.m
This should run in parallel and create 193 slices of output. These slices can be put together using combineSlices.m. Then run makeImages.m, runFDRCorrection.m, and then toBucket.sh. You may need to edit toBucket.sh to correspond with the naming of your output files.
Several of these steps are combined in runPostProcessing.m. You will need to run toBucket.sh afterwards
Visualization and thresholding can then be performed using AFNI